## Slide 1: Hazardous Waste Standards for CESQG and SQG Compliance Assurance Northeast District

## Slide 2: Generator Status
Conditionally Exempt SQG (CESQG)
  Generates < 100 kg/mo (~1/2 drum) and < 1kg P waste
  May not accumulate more than 1,000 kg (~5 drums) at one time
Small Quantity Generator (SQG)
  Generates 100 kg/mo to 1,000 kg/mo (between ~1/2 drum and 5 drums)
  May not accumulate more than 6,000 kg (~30 drums)
Large Quantity Generator (LQG)
  Generates > 1,000 kg/mo (~5 drums) and/or > 1kg P waste

## Slide 3: Conditionally Exempt Small Quantity Generators

## Slide 4: CESQG Requirements
Conditionally Exempt Small Quantity Generator (CESQG)
  Generates < 100 kg/mo (~1/2 drum) and < 1kg P waste
  Performs a hazardous waste determination [40 Code of Federal Regulations (CFR) 262.11]
  May not accumulate more than 1,000 kg (~5 drums) at one time [40 CFR 261.5(g)(2)]
Notes: If a CESQG accumulates >1000 kilograms, then it becomes a SQG

## Slide 5: CESQG Requirements (a)
Conditionally Exempt Small Quantity Generator (CESQG)
  Ensure delivery of hazardous waste to a proper facility [40 CFR 261.5(g)(3)]
  Keep records documenting proper disposal [62-730.030(3) and (4), Florida Administrative Code (FAC)]
Notes: If a CESQG accumulates >1000 kilograms, then it becomes a SQG

## Slide 6: CESQGs Next Door
Notes: There are thousands of CESQGs. Small auto shops, dry cleaners, collision shops, small manufacturing, etc.

## Slide 7: Solvent Parts Washer
Notes: One parts washer may make a facility a CESQG.

## Slide 8: CESQG – Failing to Ensure Proper Disposal of D001 Paint
40 CFR 261.5(g)(3)
Notes: One of the most common violation is failure to ensure proper disposal of hazardous waste. This facility threw D001 waste paint in to the dumpster.

## Slide 9: Small Quantity Generators

## Slide 10: SQG Generator Status
  Generates 100 kg/mo to 1,000 kg/mo (~1/2 drum to 5 drums) [40 CFR 262.34(d)]
  May not accumulate more than 6,000 kg (~30 drums) [40 CFR 262.34(d)(1)]

## Slide 11: Solvent Parts Washer (a)
Notes: One large parts washer may make a facility a SQG – it depends 1) is spent solvent hazardous waste; and 2) how many gallons of spent solvent the parts washer holds. Two or more parts washers may make a facility a SQG depending on when they are changed out.

## Slide 12: 40 CFR 262 Subpart A – General Standards
Perform a hazardous waste determination [40 CFR 262.11]
Notify the DEP and obtain an EPA/DEP identification number [40 CFR 262.12] using form 8700-12FL
Notes: Florida Handler Search: https://fldeploc.dep.state.fl.us/rcra_epa/CHAZreports/handler_sel.asp
Request notify closed/moved/change in status

## Slide 13: 40 CFR 262 Subpart B – The Manifest
Use a Uniform Hazardous Waste Manifest [40 CFR 262.20(a)(1)]
May use tolling agreement instead of manifest
Notes: Include generator EPA/DEP identification number
Example of tolling agreement = precious metals reclaimed for return to the facility and put back in process
- The uniform manifest will consist of six (6) pages:
o Page 1 (top copy): “Designated facility to destination State (if required)”
o Page 2: “Designated facility to generator State (if required)”
o Page 3: “Designated facility to generator”
o Page 4: “Designated facility’s copy”
o Page 5: “Transporter’s copy”
o Page 6 (bottom copy): “Generator’s initial copy”

## Slide 14: SQG Improperly Managing Waste
Notes: Open containers evaporating waste is not ensuring proper disposal

## Slide 15: SQG – Disposal Without a Manifest
40 CFR 262.11 and/or 40 CFR 262.20
Notes: Disposal of hazardous waste without a manifest
Dumpster diving!

## Slide 16: Hazardous Waste in Trash
Notes: HW solvents and paint/alodine brushes are thrown away into the trash.

## Slide 17: 40 CFR 262 Subpart C – Accumulation Requirements
Hazardous waste should be accumulated in containers [40 CFR 262.34(a)(1)(i)]
Hazardous waste may be accumulated in tanks if the requirements of 40 CFR 265.201 are met

## Slide 18: 40 CFR 262 Subpart C – Accumulation Requirements (a)
SQGs may accumulate waste for 180 days [40 CFR 262.34(d)]
A one time 30-day extension may be granted by DEP under unusual circumstances [40 CFR 262.34(b)]
A SQG may accumulate up to 6,000 kgs of hazardous waste at one time [40 CFR 262.34(d)(1)]

## Slide 19: SQG Containers

## Slide 20: SQG Container Dates
Marked with date of accumulation

## Slide 21: Container Labels
Labeled “Hazardous Waste”

## Slide 22: SQG – Satellite Container

## Slide 23: Satellite Container
Good – closed and labeled

## Slide 24: Satellite Container (a)
Good – closed and labeled

## Slide 25: SQG – Satellite Container?
No label, open container, poor condition
40 CFR 262.34(c)(1)(ii); 40 CFR 262.34(c)(1)(i)

## Slide 26: SQG – Satellite Container? (a)

## Slide 27: Satellite to Dated Accumulation Containers Only
Notes: Can not place waste from satellite into another satellite. 2nd drum must be a dated drum.

## Slide 28: SQG – Container Condition
40 CFR 265.171

## Slide 29: SQG – Container Condition
40 CFR 265.171

## Slide 30: SQG Container Condition
Good condition - 40 CFR 265.171
Notes: 265.171
Good condition

## Slide 31: SQG Container Management
40 CFR 265.173(a)
Notes: open

## Slide 32: SQG – Closed Container?
40 CFR 265.173(a)
Notes: Open because the funnel just slips into the bung. It does not screw in.

## Slide 33: SQG – Closed Container? (a)
40 CFR 265.173(a)

## Slide 34: SQG – Container Management
40 CFR 265.173(b)

## Slide 35: SQG Container Management (a)
40 CFR 265.173(b)

## Slide 36: SQG – Container Management (b)
40 CFR 265.173(b)
Notes: No telling what is in these containers – now “unknown” waste that requires costly sampling??

## Slide 37: SQG – Container Aisle Space
40 CFR 265.35
and 62-730.160(7), FAC
Notes: insufficient

## Slide 38: SQG - Container Aisle Space
40 CFR 265.35 and 62-730.160(7), FAC
Notes: good

## Slide 39: SQG Container Aisle Space
Good – adequate aisle space
40 CFR 265.35; 62-730.160(7), FAC
Notes: Good aisle space

## Slide 40: SQG - Tanks
Label “Hazardous Waste” [40 CFR 262.34(a)(3)]
Document 180 day storage limit compliance [40 CFR 262.34(d)]
Comply with 40 CFR 265.201 (SQG)
Notes: IBC totes are not tanks.

## Slide 41: 40 CFR 262 Subpart C – Emergency Coordinator
40 CFR 262.34(d)(5)(i)
  Have at least one designated coordinator
  Coordinates all emergency response measures
  Either on premises or short distance away

## Slide 42: 40 CFR 262 Subpart C – Modified Contingency Plan
40 CFR 262.34(d)(5)(ii)

## Slide 43: 40 CFR 262 Subpart C – Personnel Training
40 CFR 262.34(d)(5)(iii)

## Slide 44: SQG – Personnel Training
40 CFR 262.34(d)(5)(iii)

## Slide 45: 40 CFR 265 Subpart C – Preparedness and Prevention
Maintenance and Operation [40 CFR 265.31]
Minimize the possibility of fire, explosion, or release of hazardous waste or hazardous waste constituents to the air, soil, surface, or groundwater

## Slide 46: SQG – Maintenance and Operation
Facility must be properly maintained and operated [40 CFR 265.31]

## Slide 47: SQG – Maintenance and Operation (a)
Facility must be properly maintained and operated [40 CFR 265.31]

## Slide 48: SQG – Maintenance and Operation (b)

## Slide 49: 40 CFR 265 Subpart C – Required Equipment
Internal communications or alarm equipment [40 CFR 265.32(a)]
Telephone or two-way radio [40 CFR 265.32(b)]
Fire equipment [40 CFR 265.32(c)]

## Slide 50: 40 CFR 265 Subpart C – Required Equipment (a)
Spill control/decontamination equipment [40 CFR 265.32(c)]
Water or foam available at adequate volume or pressure [40 CFR 265.32(d)]

## Slide 51: 40 CFR 265 Subpart C – Required Equipment (b)
Notes: Can you find the safety shower here?

## Slide 52: 40 CFR 265 Subpart C – Required Equipment (c)

## Slide 53: 40 CFR 265 Subpart C – Required Equipment (d)
[40 CFR 265.33]
Equipment Maintenance

## Slide 54: 40 CFR 265 Subpart C – Emergency Arrangements
Make arrangements with the local authorities
  [40 CFR 265.37]
Please document and keep copies
Notes: We have a form letter that we give to facilities as an example.

## Slide 55: 40 CFR 262 Subpart D – Recordkeeping and Reporting
Exception reports required [40 CFR 262.42(b)] if a copy of the manifest is not received within 60 days
Test results – for example TCLP [40 CFR 262.11]

## Slide 56: 40 CFR 262 Subpart D – Recordkeeping and Reporting (a)
Weekly container inspections [40 CFR 265.174]
Container inspection records [Rule 62-730.160(6), F.A.C.]
    Date
    Time
    Legibly written name of the inspector
    Number of containers
    Condition of containers
    Notes of observations made, date and nature of repairs or corrective actions

## Slide 57: 40 CFR Part 268 Land Disposal Restrictions (LDR)
LDR waste analysis
LDR notification
LDR certification
LDR waste analysis plan
Retain documentation for three years

## Slide 58: LDR Notice Contents
All applicable waste codes
Treatability group
Constituents subject to regulation, if not all regulated constituents
Manifest document number of shipment
Waste analysis data where available
One time notice pursuant to Phase IV LDR dated 5/12/97 (62 FR 25998-26040)

## Slide 59: Questions?
Contact Compliance Assurance
Hazardous Waste Program
Northeast District
8800 Baymeadows Way West
Suite 100 Jacksonville, Florida 32256 (904) 256-1700 phone (904) 256-1588 fax